## Slide 1
Fuzzy Logic Systems
A Worked Case Study: Designing a Smart Engine Cooling System Controller
Course: Fuzzy Logic & Intelligent Control Systems
Inputs (3) · Output (1) · Mamdani FIS

## Slide 2
The Problem: Why Does Engine Cooling Need Fuzzy Logic?
Fuzzy Logic PBL Module
Slide 02
Scenario & Traditional Failure
A vehicle's engine operates under dynamic stress. A simple binary thermostat rule like "If Coolant Temp > 90°C, turn on fan for 10 min" is brittle. It ignores whether the ambient weather is 40°C in traffic or 10°C on a highway, leading to thermal shock, excessive fan wear, or engine overheating.
Human automotive engineers reason with soft thresholds: "Engine is moderately hot," "Coolant is rising fast," "Environment is scorching." Fuzzy logic mimics this expert reasoning seamlessly.
Design Task & Learning Objectives
Design Task: Build a Mamdani Fuzzy Inference System (FIS) reading Engine Temp, Coolant Temp, and Environmental Temp to dictate precise Radiator Fan Duration.
•
Differentiate crisp vs. fuzzy engine states
•
Design membership functions for thermal sensors
•
Fuzzify real-time temperature sensor telemetry
•
Evaluate Mamdani min/max IF-THEN rule bases
•
Defuzzify the aggregated output using the Centroid method

## Slide 3
Crisp Sets vs. Fuzzy Sets in Thermal Systems
Fuzzy Logic PBL Module
Slide 03
Crisp (Classical) Thermal Set
Membership is strictly binary: an engine state either completely belongs (1) or does not belong (0).
Problem: A tiny 0.2°C noise spike abruptly toggles heavy fan power, causing electromechanical stress and hunting behavior.
Fuzzy Thermal Set
Membership is a continuous degree: , enabling smooth, gradual transitions between states.
Advantage: An engine reading can be somewhat warm and somewhat hot simultaneously, matching realistic thermodynamics.

## Slide 4
Architecture of Fuzzy Inference System (FIS)
Fuzzy Logic PBL Module
Slide 04
1. Fuzzification
Convert crisp sensor inputs (°C) into fuzzy membership degrees using input membership functions.
2. Rule Inference
Apply expert IF-THEN rules from Knowledge Base; evaluate antecedents with min/max Mamdani logic.
3. Aggregation
Combine all fired rule output shapes into one comprehensive fuzzy output area envelope.
4. Defuzzification
Convert aggregated fuzzy output curve into a single crisp value: Radiator Fan Duration (minutes).

## Slide 5
Formal Definition of a Fuzzy Set
Fuzzy Logic PBL Module
Slide 05
A fuzzy set A defined on a universe of discourse X is represented as a set of ordered pairs mapping element values to membership degrees:
Universe of Discourse (X): The entire crisp physical range, e.g., Engine Temp .
Membership Function : Curve assigning every crisp temperature x a grade between 0 and 1.
Continuous Notation: (Where '/' represents association notation, not algebraic division).
Discrete Notation:

## Slide 6
Key Properties of a Fuzzy Set
Fuzzy Logic PBL Module
Slide 06
Support
The set of all domain temperature values having non-zero membership grade.
Core
Domain region representing complete, unquestionable set membership.
Alpha-Cut ( -Cut)
Crisp threshold set containing all elements with membership degree ≥ α.

## Slide 7
Common Types of Membership Functions
Fuzzy Logic PBL Module
Slide 07
 | Parameters | Mathematical Formula | Automotive System Application
Triangular | a, b, c |  | Standard for Engine/Coolant Temp MFs (fast, lightweight microcontroller calculation).
Trapezoidal | a, b, c, d |  | Plateau ranges like "Normal Operating Range" (75°C–90°C full stability).
Gaussian | c, σ | exp ( - 1 2 ( x - c σ ) 2 ) | Smooth differentiable curves in high-precision adaptive ANFIS controllers.
Sigmoidal | a, c | 1 1 + exp ( - a ( x - c ) ) | Open-ended boundaries like "Extreme Engine Overheating (>110°C)".

## Slide 8
Fuzzy Set Operations (Zadeh Operators)
Fuzzy Logic PBL Module
Slide 08
Union (OR)
Selects maximum truth degree between antecedents. Used when multiple warning criteria trigger cooling.
Intersection (AND)
Selects minimum truth degree. Core operator for combining multi-input rule antecedents in Mamdani FIS.
Complement (NOT)
Inverts membership grade. Evaluates negation conditions, e.g., "Engine is NOT Cool".

## Slide 9
Generalized Operators: T-Norms & T-Conorms
Fuzzy Logic PBL Module
Slide 09
Family | T-Norm (Generalized AND) | T-Conorm (Generalized or) | Engineering Application Contex
Zadeh (Standard) |  |  | Standard choice for this PBL module robust, computationally fast on embedded ECUs
Algebraic/Probabilistic |  |  | Produces smooth output interaction surfaces: sensitive to all input fluctuations.
Bounded (Łukasiewicz) |  |  | Strict boundary control logic used in safety-critical acrospace/automotive systems

## Slide 10
Linguistic Variables & Linguistic Hedges
Fuzzy Logic PBL Module
Slide 10
Linguistic Variables
Variables expressed in human words rather than pure numbers. In our thermal system:
Linguistic Hedges
Hedges modify membership functions mathematically without adding new rules:
Engine Temp ∈ {Cool, Normal, Hot}
Coolant Temp ∈ {Low, Normal, High}
Environmental Temp ∈ {Cold, Mild, Hot}
Fan Duration ∈ {Off, Short, Medium, Long}
Concentration ("very"): Narrows set — e.g., "Very Hot Engine" requiring immediate max cooling.
Dilation ("somewhat"): Widens set — e.g., "Somewhat High Coolant Temp".

## Slide 11
Mamdani vs. Sugeno (TSK) Inference
Fuzzy Logic PBL Module
Slide 11
Aspect | Mamdani Inference (Used in this Module) | Sugeno / TSK Inference
Rule Consequent | Fuzzy set membership curve ("THEN Fan Duration is LONG") | Mathematical function of inputs ("THEN Duration = 0.5·E_Temp + 0.3·C_Temp")
Output State | Fuzzy region requiring full aggregation | Crisp value per rule (weighted average sum)
Interpretability | Very High — Expert human readable | Moderate — Mathematical equation
Computation | Integration across output space | Fast linear algebraic evaluation

## Slide 12
Designing the Smart Engine Cooling FIS
Comprehensive 6-Step Implementation: Input Temperature Telemetry → Fuzzy Rule Engine → Actuator Control
Fuzzy Logic PBL Module
Slide 12

## Slide 13
Identify Linguistic Variables & Terms
Fuzzy Logic PBL Module
Slide 13
Variable | Role | Universe of Discourse (X) | Linguistic Terms | Unit
Engine Temperature | Input 1 | 0 to 120 | Cool, Normal, Hot | °C
Coolant Temperature | Input 2 | 0 to 120 | Low, Normal, High | °C
Environmental Temp | Input 3 | 0 to 50 | Cold, Mild, Hot | °C
Radiator Fan Duration | Output | 0 to 30 | Off, Short, Medium, Long | Minutes

## Slide 14
Membership Functions: Engine Temperature
Fuzzy Logic PBL Module
Slide 14
Engine Temperature ranges from 0°C to 120°C. Fuzzified into 3 triangular/trapezoidal linguistic sets:
Term | Parameters (a, b, c) | Range (°C)
Cool | a=0, b=0, c=70 | 0°C – 70°C
Normal | a=50, b=80, c=100 | 50°C – 100°C
Hot | a=85, b=115, c=120 | 85°C – 120°C

## Slide 15
Membership Functions: Coolant Temperature
Fuzzy Logic PBL Module
Slide 15
Coolant Temperature measures direct thermal energy in the engine fluid loop across 0°C to 120°C:
Term | Parameters (a, b, c) | Interpretation
Low | a=0, b=0, c=60 | Cold start fluid state
Normal | a=40, b=75, c=95 | Optimal thermal operational loop
High | a=80, b=110, c=120 | Coolant heat saturation threat
Overlap Region: Between 80°C and 95°C, coolant belongs to both Normal and High.
Safety Cushion: Prevents premature fan shutdown while thermal fluid remains saturated.

## Slide 16
Membership Functions: Environmental Temperature
Fuzzy Logic PBL Module
Slide 16
Ambient outdoor weather temperature across 0°C to 50°C directly alters ambient convective cooling rates:
Term | Parameters (a, b, c) | Ambient Condition
Cold | a=0, b=0, c=20 | Winter weather (≤ 20°C)
Mild | a=10, b=25, c=38 | Moderate climate (10°C–38°C)
Hot | a=30, b=50, c=50 | Scorching heat (≥ 30°C)
Convective Impact: High environmental heat impairs natural radiator heat dissipation, demanding longer active fan assistance.

## Slide 17
Output Variable: Radiator Fan Duration
Fuzzy Logic PBL Module
Slide 17
Actuator control output determining fan run-time from 0 to 30 minutes:
Output Term | Parameters (a, b, c) | Peak Center
Off | a=0, b=0, c=5 | 0 min
Short | a=3, b=8, c=15 | 8 min
Medium | a=10, b=18, c=25 | 18 min
Long | a=20, b=28, c=30 | 28 min
Radiator Fan Control
Fuzzy Controller
Fan ON / OFF + operating duration
Output: Fan duration from 0 to 30 minutes

## Slide 18
Fuzzy IF-THEN Rule Base
Fuzzy Logic PBL Module
Slide 18
Rule ID | Engine Temp (IF) | Coolant Temp (AND) | Env Temp (AND) | Radiator Fan Duration (THEN)
R1 | Hot | High | Hot | Long
R2 | Hot | High | Mild | Long
R3 | Hot | Normal | Hot | Medium
R4 | Normal | High | Hot | Medium
R5 | Normal | Normal | Mild | Short
R6 | Cool | Low | Cold | Off
R7 | Normal | Low | Cold | Off
R8 | Cool | High | Hot | Short
Note: The 8 rules shown are representative core rules for the worked example. A complete deployment should ensure coverage of all relevant input combinations.

## Slide 19
Fuzzy Inference: The Mamdani Method
Fuzzy Logic PBL Module
Slide 19
1. Antecedent Evaluation
Read membership degrees for all inputs from live sensor values.
2. Operator Evaluation (AND)
Combine multiple antecedents using minimum function (Zadeh T-norm):
3. Implication / Clipping
Truncate output term membership curve at rule firing strength w:

## Slide 20
Fuzzify Live Sensor Readings
Live Telemetry Snapshot: Engine Temp = 92°C | Coolant Temp = 88°C | Environmental Temp = 35°C
Fuzzy Logic PBL Module
Slide 20
Sensor Reading | Linguistic Term | Calculation | Membership Degree (μ)
Engine Temp = 92°C | Normal (50, 80, 100) Hot (85, 115, 120) | (100 - 92) / (100 - 80) (92 - 85) / (115 - 85) | 0.400 0.233
Coolant Temp = 88°C | Normal (40, 75, 95) High (80, 110, 120) | (95 - 88) / (95 - 75) (88 - 80) / (110 - 80) | 0.350 0.267
Environmental = 35°C | Mild (10, 25, 38) Hot (30, 50, 50) | (38 - 35) / (38 - 25) (35 - 30) / (50 - 30) | 0.231 0.250

## Slide 21
Evaluate Firing Rules
Fuzzy Logic PBL Module
Slide 21
Rule | Antecedent Calculation (AND → min) | Firing Strength (w) | Clipped Output Term
R1: Hot AND High AND Hot | min(μ_Hot: 0.233, μ_High: 0.267, μ_HotEnv: 0.250) | 0.233 | Long
R2: Hot AND High AND Mild | min(μ_Hot: 0.233, μ_High: 0.267, μ_MildEnv: 0.231) | 0.231 | Long
R3: Hot AND Normal AND Hot | min(μ_Hot: 0.233, μ_NormCool: 0.350, μ_HotEnv: 0.250) | 0.233 | Medium
R4: Normal AND High AND Hot | min(μ_NormEng: 0.400, μ_High: 0.267, μ_HotEnv: 0.250) | 0.250 | Medium
R5: Normal AND Normal AND Mild | min(μ_NormEng: 0.400, μ_NormCool: 0.350, μ_MildEnv: 0.231) | 0.231 | Short

## Slide 22
Aggregation & Defuzzification Theory
Fuzzy Logic PBL Module
Slide 22
Step 5: Aggregation
Merges all fired rule output shapes into a single combined fuzzy set using maximum operator:
Step 6: Defuzzification
Converts the aggregated fuzzy output into a crisp fan run-time using Centroid Defuzzification:

## Slide 23
Aggregate Outputs & Defuzzify
Fuzzy Logic PBL Module
Slide 23
16.72
minutes fan run-time
Worked example
Engine 92°C | Coolant 88°C | Ambient 35°C
Output term | Firing strength | Peak center
Short | 0.231 | 8 min
Medium | 0.250 | 18 min
Long | 0.233 | 28 min
Centroid: y* = ∫ y μagg(y)dy / ∫ μagg(y)dy ≈ 16.72 min
Aggregated clipped output: Short 0.231, Medium 0.250, Long 0.233.
Important correction
19.79 min was a weighted peak average, not the true Mamdani centroid. The corrected centroid result is 16.72 min.

## Slide 24
Why Fuzzy Logic Suits Engine Cooling
Fuzzy Logic PBL Module
Slide 24
Prevents Thermal Shock
Reduces abrupt ON/OFF decisions by varying the commanded fan operating duration according to thermal conditions.
Energy Efficiency
Can reduce unnecessary fan operation by adapting the commanded duration to engine, coolant, and ambient temperatures.
Multi-Sensor Tradeoffs
Balances competing inputs automatically (e.g., hot engine vs. cold ambient air on a highway drop).

## Slide 25
PBL Activity: Extend the Engine Cooling FIS
Fuzzy Logic PBL Module
Slide 25
1. Re-fuzzify by Hand: Given Engine Temp = 105°C, Coolant Temp = 92°C, Env Temp = 20°C, compute membership degrees and identify firing rules.
2. Add 4th Input (Vehicle Speed): Introduce Vehicle Speed (Stopped / City / Highway). High speed creates ram-air cooling—how should rule outputs adjust?
3. Tune Breakpoints: Modify "Hot" membership breakpoints for heavy desert towing vs. arctic winter driving conditions.
4. Genetic Algorithm Integration: Propose how a Genetic Algorithm (GA) could automatically optimize membership function parameters.

## Slide 26
Image Sources
https://www.sdzcn.com/uploads/image/20220729/13/automotive-temperature-sensor.jpg
Source: www.sdzcn.com
https://lookaside.fbsbx.com/lookaside/crawler/media/?media_id=4322154114693673
Source: www.facebook.com